## Slide 1: IIoT System Protocols
Unit II

## Slide 2: Sensors
Sensors are devices that detect and measure physical properties, conditions, or events in the industrial environment. They convert these measurements into electrical signals or digital data that control systems can process. Some common types of sensors used in industrial automation include:
Proximity Sensors: These sensors detect the presence or absence of an object or the proximity of an object to a specified point. Examples include inductive sensors, capacitive sensors, and ultrasonic sensors.
Temperature Sensors: These sensors measure temperature and are crucial for monitoring and controlling temperature-dependent processes. Examples include thermocouples and resistance temperature detectors (RTDs).
Pressure Sensors: Pressure sensors measure pressure levels in various industrial processes to ensure safety and efficiency. Examples include piezoelectric pressure sensors and strain gauge pressure sensors.
Flow Sensors: Flow sensors measure the rate of fluid or gas flow in pipes or channels, enabling precise control of material flow. Examples include electromagnetic flow meters and ultrasonic flow sensors.
Level Sensors: Level sensors determine the height or level of liquid or solid materials in tanks or containers. Examples include float switches, capacitance level sensors, and ultrasonic level sensors.
Position Sensors: Position sensors provide information about the position and movement of objects, which is essential in robotics and automation. Examples include encoders and potentiometers.
Vision Sensors: Vision sensors use cameras and image processing techniques to detect and identify objects, inspect quality, and guide robots in manufacturing processes.

## Slide 3: Actuators used for Industrial Processes
Actuators: Actuators receive control signals from the automation system and perform physical actions or movements in response. They translate electrical or digital commands into mechanical motion, making it possible to control industrial processes. Common types of actuators used in industrial automation include:
Electric Motors: Electric motors convert electrical energy into mechanical motion and are used for driving conveyors, pumps, fans, and various machinery.
Pneumatic Actuators: Pneumatic actuators use compressed air to generate linear or rotary motion. They are often used in applications where fast and precise movements are required.
Hydraulic Actuators: Hydraulic actuators use pressurized hydraulic fluid to generate mechanical motion. They are suitable for heavy-duty applications that require high force.
Solenoid Valves: Solenoid valves control the flow of fluids or gases by opening or closing passages when an electrical signal is applied.
Servo Motors: Servo motors are specialized electric motors that offer precise control over position, velocity, and torque, making them ideal for robotics and CNC machines.

## Slide 4: Roles of sensors and actuators in IIOT
IIoT sensors provide 24/7 monitoring of critical equipment instead of relying on periodic manual checks. This can be especially valuable in collecting data from assets that are remotely located. Sensor alerts can be sent to scattered equipment and gathered in a centralized computer system.
Sensors also reduce labor costs in equipment monitoring. By triggering less expensive preventive maintenance tasks, sensors can reduce the amount spent on major problems or emergency repairs.
Sensors data can be sent to a computerized maintenance management system (CMMS) for analysis. This allows maintenance managers to look at historic trends of particular assets, as well as pinpoint failure spots and frequency. This integration of data generates the information to make better future business decisions.

## Slide 5: Roles of actuators in IIOT
Actuators play a critical role in the Industrial Internet of Things (IIoT), serving as the bridge between the digital and physical worlds. They are essential components that convert electrical signals into physical actions, enabling automation and control within industrial processes.
Actuators are fundamental to automation, allowing IIoT systems to control machinery and processes without human intervention.
Smart actuators in IIoT systems often include features for optimizing energy use
Actuators can also be sources of valuable data. By monitoring their operation and environmental conditions, they contribute to a larger dataset that can be analyzed to improve processes, enhance performance, and innovate new solutions.

## Slide 6: IIOT Sensor networks
Internet of Things (IoT) devices are low power, battery-operated and capable of connecting to the Internet via a communications network.
Depending on the environment and usage requirements, each technology has strengths and weaknesses concerning cost, range, scalability and network-specific connectivity. Range performance divides the technologies into those that operate in Local Area Networks (LANs) and Low Power Wide Area Networks (LPWANs). Wi-Fi, Bluetooth/BLE, Zigbee, Z-Wave and Thread are classed as LANs operating with ranges under 100m. LPWANs, cellular and Wi-Fi HaLow™ have coverage up to 10km and beyond. LANs typically handle constant high bandwidth rates, while LPWANs deliver small blocks of data at low bandwidth rates, additionally dealing with geographical location issues and network congestion.

## Slide 7: Process automation on IIoT Platform
Process automation on an IIoT (Industrial Internet of Things) platform involves using interconnected devices, sensors, and software to automate and optimize industrial processes. Here’s an in-depth look at the key components and steps involved in process automation on an IIoT platform:
1. Sensors and Data Acquisition
Sensors: Collect real-time data from various industrial processes (e.g., temperature, pressure, vibration).
Edge Devices: Aggregate and pre-process data from multiple sensors to reduce latency and bandwidth usage.
Data Acquisition Systems: Gather data from edge devices and transmit it to central systems for further processing.
2. Communication Networks
Wired Networks: Ethernet, Modbus RTU, Profibus for reliable and high-speed data transfer.
Wireless Networks: Wi-Fi, Bluetooth, Zigbee, LoRaWAN for flexible and scalable connectivity.
Cellular Networks: 4G/5G for remote and wide-area applications.
3. Data Processing and Storage
Edge Computing: Performing real-time data analysis and decision-making at the edge to minimize latency.
Cloud Computing: Leveraging cloud platforms for scalable data storage and advanced analytics.
Data Lakes and Warehouses: Storing vast amounts of data for historical analysis and machine learning.

## Slide 8
4. Automation Control Systems
Programmable Logic Controllers (PLCs): Control industrial processes by executing pre-programmed instructions.
Distributed Control Systems (DCS): Manage complex, large-scale processes by distributing control functions.
Supervisory Control and Data Acquisition (SCADA): Monitor and control industrial processes remotely.
5. Advanced Analytics and Machine Learning
Real-time Analytics: Continuously analyzing data to detect anomalies and optimize processes.
Predictive Maintenance: Using historical data and machine learning algorithms to predict equipment failures and schedule maintenance proactively.
Optimization Algorithms: Applying algorithms to improve efficiency, reduce waste, and enhance productivity.
6. Automation Software and Platforms
Manufacturing Execution Systems (MES): Manage and monitor manufacturing operations on the shop floor.
Enterprise Resource Planning (ERP): Integrate and manage core business processes, such as inventory and production planning.
Industrial IoT Platforms: Centralize data from various sources, providing tools for analytics, visualization, and automation.a

## Slide 9
7. Human-Machine Interfaces (HMI)
Dashboards and Visualization Tools: Provide real-time insights and control over industrial processes.
User Interfaces: Allow operators to interact with automation systems, adjust settings, and respond to alerts.
8. Security and Compliance
Data Encryption: Secure data transmission and storage using encryption protocols.
Access Control: Implement robust authentication and authorization mechanisms.
Regulatory Compliance: Ensure adherence to industry standards and regulations (e.g., ISO, NIST).
9. Interoperability and Integration
Standard Protocols: Use industry-standard protocols (OPC-UA, MQTT) to ensure compatibility between devices and systems.
APIs and Middleware: Facilitate integration with existing enterprise systems and third-party applications.
Interoperability Frameworks: Implement frameworks that enable seamless communication between diverse systems and devices.
10. Continuous Improvement and Scalability
Feedback Loops: Establish continuous feedback loops to monitor and improve automation processes.
Scalability: Design systems that can scale with the growth of operations and the addition of new devices and technologies.
Innovation and Upgrades: Stay updated with the latest advancements in IIoT and automation technologies to continuously enhance capabilities.

## Slide 10: Data Acquisitions on IIoT Platform
Data acquisition on an Industrial Internet of Things (IIoT) platform involves collecting data from various industrial assets, sensors, and systems to enable advanced analytics, monitoring, and automation. Here’s a detailed overview of the data acquisition process on an IIoT platform:
1. Data Sources Sensors and Actuators: Devices that measure various physical parameters (temperature, pressure, humidity, etc.) and control industrial processes.
Machines and Equipment: Data from CNC machines, robots, conveyors, and other industrial machinery.
Legacy Systems: Integration with existing industrial control systems like SCADA, PLCs, and DCS.
Edge Devices: Smart gateways and edge computers that pre-process data before sending it to the cloud.
2. Data Collection Methods
Direct Sensor Connectivity: Sensors connected directly to the IIoT platform via wired or wireless connections.
Gateways and Edge Computing: Edge devices aggregate data from multiple sensors and provide preliminary processing.
Protocol Translation: Converting data from proprietary industrial protocols (Modbus, OPC-UA, MQTT) into a standardized format.
APIs and Middleware: Using APIs to collect data from software systems and databases.

## Slide 11
3. Data Transmission
Wired Connections: Ethernet, Modbus RTU, and other industrial communication standards.
Wireless Communication: Wi-Fi, Bluetooth, Zigbee, LoRaWAN, NB-IoT, and other wireless protocols.
Cellular Networks: 4G/5G networks for remote or mobile industrial applications.
4. Data Processing and Storage
Edge Processing: Performing real-time data analysis, filtering, and aggregation at the edge to reduce latency and bandwidth usage.
Cloud Storage: Sending processed and raw data to the cloud for long-term storage and advanced analytics.
Data Lakes and Warehouses: Storing vast amounts of structured and unstructured data for historical analysis and machine learning.

## Slide 12
5. Data Security and Privacy
Encryption: Secure data transmission using encryption protocols like TLS/SSL.
Authentication and Authorization: Ensuring only authorized devices and users can access the data.
Data Anonymization: Protecting sensitive information by anonymizing data before analysis.
6. Data Integration and Interoperability
APIs and Connectors: Facilitating integration with enterprise systems (ERP, MES, CRM).
Standards and Protocols: Adopting industry standards (ISA-95, ISO/IEC 30141) for interoperability.
Middleware Solutions: Using middleware to bridge different systems and protocols.
7. Data Analytics and Visualization
Real-time Analytics: Monitoring and analyzing data in real-time to detect anomalies and optimize operations.
Predictive Maintenance: Using historical data and machine learning to predict equipment failures before they occur.
Dashboards and Reports: Visualizing data through dashboards and generating reports for decision-makers.

## Slide 13: Wireless Communication Technologies
Wireless communication plays a significant role in day-to-day life. Besides communication, wireless technology has become an integral part of our daily activities. The transmission of data or information from one place to another wirelessly is referred to as wireless communication. This provides an exchange of data without any conductor through RF and radio signals. The information is transmitted across the devices over some meters to hundreds of kilometers through well-defined channels.
The term wireless refers to the communication or transmission of information over a distance without requiring wires, cables, or any other electrical conductors. Wireless communication is one of the important mediums of transmission of data or information to other devices. The Communication is set and the information is transmitted through the air, without requiring any cables, by using electromagnetic waves like radio frequencies, infrared, satellite, etc., in a wireless communication technology network.

## Slide 14: ZigBee and ZigBee IP
ZigBee is a wireless communication standard designed to address the unique needs of low-power, low-cost wireless sensor, and control networks. ZigBee can be used almost anywhere, as it is easy to implement and requires little power to operate. Zigbee has been developed looking into the needs of the communication of data with a simple structure like the data from the sensors.
ZigBee devices are designed for low-power consumption.
ZigBee is used in Commercial Applications like sensing and monitoring applications.
ZigBee uses extremely long device battery life.
ZigBee gives the flexibility to do more with reliable wireless performance and battery operation.
ZigBee IP is the first IPv6-based open standard for a full wireless mesh networking solution. It is an upgraded version of Zigbee designed to control and connect many different low-power devices into a single control network, enabling seamless integration with IP-based networks.

## Slide 15: Z-Wave
Z-Wave is a wireless communication protocol known for Home Automation.
Z-wave is not entirely open-source, but several segments of the technology were made public.
Z-wave devices are designed to be compatible with each other, regardless of their type, brand, manufacturer or version.
Z-wave chips are optimized for battery-powered devices, ensuring low power consumption and consequently long battery life.
Z-wave runs using radio waves at the frequency of 800-900 MHz.
Z-wave has built-in Security 2 framework

## Slide 16: Wi-Fi Backscatter
A novel communication system that bridges RF-powered devices with the Internet.
It has three actors: a Wi-Fi reader, a Wi-Fi helper, and a RF-powered device (Wi-Fi Backscatter tag).
The reader and helper can be any commodity WiFi device, including routers and mobile devices.
The Wi-Fi reader leverages the channel information from the Wi-Fi helper's packets to decode the transmissions from the tag.

## Slide 17: NFC
Near Field Communication (NFC) is a set of short-range wireless technologies, typically requiring a distance of 10 cm or less to initiate a connection. NFC lets you share small payloads of data between an NFC tag and an Android-powered device, or between two Android-powered devices.
Low Power consumption
Range up to 10 cm
Faster connectivity
Slow Data transfer speed
Suitable for passive devices like tags and advertising signs
Applications: Mobile payments

## Slide 18: 6LoWPAN (IPv6 over Low-Power Wireless Personal Area Networks)
6LoWPAN is a mesh network that is robust, scalable, and can heal on its own.
It delivers low-cost and secure communication in IoT devices.
It can be directly routed to cloud platforms.
It offers one-to-many and many-to-one routing.
In the network, leaf nodes can be in sleep mode for a longer duration of time.
every node has its own IPv6 address. This allows the node to connect directly with the Internet using open standards.
6LoWPAN is essentially a new competitor for Zigbee.
6LoWPAN is an IP-based network like WiFi.
6LoWPAN is primarily used for home automation applications and smart meters.

## Slide 19: RPL
RPL stands for Routing Protocol for Low Power and Lossy Networks for heterogeneous traffic networks.
This protocol is based on the same standard as by Zigbee and 6 Lowpan is IEEE 802.15.4
It holds both many-to-one and one-to-one communication.
efficient and effective protocol for data routing in resource-constrained scenarios, such IoT devices as per requirement.
Scalability: The protocol can accommodate big networks with low power and lossy connectivity
Multipoint-to-point traffic generation: RPL offers a way to send data to a single destination point from several devices
Quality of Service (QoS) – by offering various methods for reliable packet delivery system and congestion control system.
Adaptive – RPL modifies the required routes in response to link quality and energy availability changes in the network environment or system.
Security system: RPL incorporates techniques for integrity protection, authentication, confidentiality, and encryption for better performance.

## Slide 20: IIoT Low Power WAN Technologies
A low-power, wide-area network (LPWAN or LPWA network) is a type of wireless telecommunication wide area network designed to allow long-range communication at a low bit rate between IoT devices, such as sensors operated on a battery.

## Slide 21: SigFox
Sigfox is an inexpensive, reliable, low-power solution to connect sensors and devices.
It utilizes a wide-reaching signal that passes freely through solid objects, called "Ultra Narrowband" and requires little energy
The network is based on one-hop star topology and requires a mobile operator to carry the generated traffic.
The signal can also be used to easily cover large areas and to reach underground objects.
Sigfox has partnered with a number of firms in the LPWAN industry such as Texas Instruments, Silicon Labs and ON Semiconductor. The ISM radio bands support limited bidirectional communication.
The existing standard for Sigfox communications supports up to 140 uplink messages a day, each of which can carry a payload of 12 octets at a data rate of up to 100 bits per second.

## Slide 22: nWave
The Nwave technology uses UNB (Ultra Narrow Band) along with SDR techniques to deliver Communication network for IoT.
The Nwave networks operate in internationally available as well as unlicensed sub-1GHz bands. It allows deep signal propagation with little power consumption.
The network co-exist with other radio networks without any issues. They can use mesh/star topologies. The networks are scalable. In Star architecture devices can Communicate directly with Base Station. The network is secure and hence user data are protected.

## Slide 23: Dash7
DASH7 provides multi-year battery life,
range of up to 2 km,
low latency for connecting with moving things,
a very small open-source protocol stack,
AES 128-bit shared-key encryption support, and
data transfer of up to 167 kbit/s.

## Slide 24: Low Power Wi-Fi
Wi-Fi HaLow operates in spectrum below 1GHz which enables good signal penetration through walls and other obstacles.
The low power demands of the technology enable Wi-Fi HaLow devices to be powered by coin-sized cell batteries for months and, in some cases, for years.
In addition, because Wi-Fi HaLow is part of the Wi-Fi family, there is no need for proprietary hubs and gateways.

## Slide 25: LTE Category-M
Long-Term Evolution Machine Type Communication
LTE-M provides a direct and secure connection to the cloud over licensed spectrum controlled by carriers
LTE-M is not as fast as a standard 4G network
LTE-M modules have low power demand requirements, deliver relatively low data rates, and transmit wireless data in the licensed spectrum domain.
LTE Cat- M1 is also an alternative to LoRa technologies
LTE Cat-M1 provides lower bandwidth than standard LTE networks, it still offers enough bandwidth to support the transmission of video and photos.
LTE Cat-M1 is compatible with the existing network it’s easy to deploy

## Slide 26: Ingenue RPMA (Random Phase Multiple Access)
RPMA penetrates literally everywhere – through the ground and concrete. Coverage of this network is high – around 400 square miles per tower. So 17 towers will give 2000 square miles of coverage. The network can also be deployed in buildings and underground.
RPMA offers 80MHz bandwidth. To support the network, a 1MHz signal is required. can support up to 40 channels simultaneously.
This technology was developed by Ingenu
It utilizes the unlicensed, globally available 2.4 GHz ISM (Industrial, Scientific and Medical) band.
It can be easily deployed anywhere in the world.
The technology offers features like low power consumption, stand-alone broadcast channel for rapid firmware updates, excellent in-building range and AES 128-bit security encryption for a variety of IoT applications.